## Slide 1: Hybrid concurrency
The end of Dennard scaling

## Slide 2: Types of concurrency
We have explored two types of concurrency
  Thread-based
  Process-based
 | Thread | Process
No concurrency |  | 
Thread-based |  | 
Process-based |  | 
Hybrid |  | 

## Slide 3: Hybrid concurrency
Hybrid concurrency uses the available hardware resources in the most efficient manner.
  Use process-based concurrency (e.g. MPI) to execute one fat process on each node
  Use thread-based concurrency (e.g. task-based algorithms) inside each process
  Use special hardware on each node
    Graphics Processing Unit (GPU)
      NVIDIA
      AMD/ATI
    Many Integrated Core (MIC)
      Intel

## Slide 4: GPU Programming
A number of different extensions and standards exist for GPU programming.
  CUDA
    Developed by NVIDIA
    Latest NVIDIA cards have ~2600 processors
  OpenCL
    Open standard for GPU development
    Supported by NVIDIA, AMD, Intel
  C++ AMP
    Microsoft standard competing with OpenCL

## Slide 5: Characteristics of GPU programming
All of the these GPU programming standards share common characteristics.
  Special compilers
  Custom libraries (e.g. memory management)
  Special compiler directives
  GPUs do not execute not x86 or x64 code
Why?
  GPUs are not good at general purpose computing
  Tend to support only inline execution, have shorter pipelines, slower clock speeds
  Very good for floating point math

## Slide 6: Application Architecture
Taking advantage of a GPU requires specific application architecture.
  Find code that is highly parallel (Amdahl's Law)
  Find processor-bound algorithms
    Cost to move memory to and from the GPU
    Cost of more complex source code
  General purpose code will suffer when executed on the GPU
  Offload model – executable runs on host, sections of code run on GPU
Bottom line: Code needs to be written for the GPU (there is still no free lunch)

## Slide 7: Using a GPU with offload
Host
CPUs
CPU 1
CPU 2
CPU 3
CPU 4
GPU 1
GPU 2
Memory copy
Computation
Memory copy

## Slide 8: Intel Many Integration core
Intel’s entry in this market is the Many Integrated Core (MIC) architecture.
  Xeon Phi is the first MIC product released
    60 general-purpose CPUs, four threads per CPU
      Similar to Atom processors
      Execute x86, x64 code
      No out of order execution
      512-bit wide registers
      Special vector processing unit
    No graphics output
    Runs custom version of Linux on the card
    Can execute Linux binaries compiled for MIC architecture

## Slide 9: Xeon Phi

## Slide 10: Xeon Phi Architecture

## Slide 11: Individual Core Architecture

## Slide 12: Vector Processing Unit

## Slide 13: Programming for the Xeon Phi
Like other GPUs, Xeon Phi supports an offload model.
  Using the Intel C++ compiler, special directives can be added to code.
  Also supports native compilation
    Compile an entire executable to run only on the Xeon Phi
    No special directives
    Concurrency support for
      Intel MPI
      Open MP
      Intel Cilk Plus extensions
      Intel Threading Build Blocks
  Let’s look at an example

## Slide 14: Digression: Nash solutions
The algorithm and we will explore categorizes Nash solutions.
  Embarrassingly parallel
  Processor-bound
  Does not do floating point calculations
  Implemented using Threading Building Blocks

## Slide 15: Nash algorithm (6x6) on Xeon Data
Number of Threads | Actual Run Time | Linear Scalability
1 | 668.07 | 668.07
2 | 341.61 | 334.04
3 | 232.12 | 222.69
4 | 174.99 | 167.02
5 | 139.35 | 133.61
6 | 116.44 | 111.35
7 | 99.91 | 95.44
8 | 87.43 | 83.51
9 | 77.79 | 74.23
10 | 70.04 | 66.81
11 | 63.47 | 60.73
12 | 58.27 | 55.67

## Slide 16: Nash algorithm (6x6) on Xeon

## Slide 17: Nash algorithm (6x6) on Xeon Phi Data
Number of Threads | Actual Run Time | Linear Scalability
1 | 4,177.10 | 4,177.10
2 | 2,111.20 | 2,088.55
4 | 1,053.28 | 1,044.27
8 | 534.01 | 522.14
16 | 267.94 | 261.07
32 | 133.46 | 130.53
60 | 71.45 | 69.62
120 | 50.09 | 34.81
240 | 48.02 | 17.40

## Slide 18: Nash algorithm (6x6) on Xeon Phi

## Slide 19: Xeon vs Xeon Phi

## Slide 20: Why is this occurring?
Recall the end of Dennard scaling.
  GPUs exhibit worse performance.
  GPUs exhibit better performance per watt.
The near future:
  More simple, slow GPU cores available
  Improvement in GPU cores for general purpose code
  Faster connection to GPU cores (for improved offload performance)